## Slide 1: Conversion of Lab Results

## Slide 2: Lab results must be converted
North Carolina State Laboratory of Public Health sends results of the sample submitted and does not convert to ug/ft2.
Lab results give the Length and Width of dust sampling areas provided and a Final Result.
Sample results for areas 12” by 12” is easy…just change the unit to ug/ft2.

## Slide 3: Let’s work through an example
A window trough clearance sample is collected from an area 3” by 24”
The final result reported from the lab is 205 ug
Comparing this to the clearance standard of 400 ug/ft2 on window troughs, does this pass clearance?

## Slide 4: We don’t know without some calculations

## Slide 5: Handy Formula
Lab result (µg) X 144 in2 = Converted Result (µg/ ft2)
Length(in) X width (in) ft2

## Slide 6: Fill in the Values
205 µg X 144 in2 = Converted Result (µg/ ft2)
3 in X 24in ft2

## Slide 7: Simplify
205 µg X 144 in2 = Converted Result (µg/ ft2)
72 in2 ft2

## Slide 8: Simplify
205 µg X 144 in2 = Converted Result (µg/ ft2)
72 in2 ft2

## Slide 9: Simplify
205 µg X 144 = Converted Result (µg/ ft2)
72 ft2

## Slide 10: Simplify
29520 µg = Converted Result (µg/ ft2)
72 ft2

## Slide 11: Done!
410 µg/ ft2 = Converted Result

## Slide 12
What looked like a clearance pass, is a failure after conversion.

## Slide 13: Your Turn
Convert results for a windowsill measuring 2.5” by 30.5” with a final result of 133 ug.
Is this a hazard?

## Slide 14: Handy Formula
Lab result (µg) X 144 in2 = Converted Result (µg/ ft2)
Length(in) X width (in) ft2

## Slide 15: Fill in the Values
133(µg) X 144 in2 = Converted Result (µg/ ft2)
30.5(in) X 2.5 (in) ft2

## Slide 16: Simplify
133(µg) X 144 in2 = Converted Result (µg/ ft2)
76.25 in2 ft2

## Slide 17: Simplify
133(µg) X 144 in2 = Converted Result (µg/ ft2)
76.25 in2 ft2

## Slide 18: Simplify
133 µg X 144 = Converted Result (µg/ ft2)
76.25 ft2

## Slide 19: Simplify
19152 µg = Converted Result (µg/ ft2)
76.25 ft2

## Slide 20: Done!
251 µg/ ft2 = Converted Result

## Slide 21
Is this a hazard?
What is the hazard level for a windowsill?

## Slide 22
A lead poisoning hazard includes any concentrations of lead dust that is equal to or greater than
250 ug/ft2 on interior windowsills.
Yes, it is a hazard

## Slide 23
Questions?

## Slide 24
Now we are really done!
(with this part)